Проект  «На границе»

В основу проекта положено создание картины движения робота-солдата на условно пограничной территории, которое, как и любое другое перемещение в установленной зоне, улавливается и фиксируется радаром. С высокой степенью точности, в заданных единицах измерения данные на радаре как от статических, так и от динамических объектов выводятся в графическом режиме  на экран.

Движение робота-солдата приводится пультом дистанционного управления. Робот, как солдат-пограничник, движется по указанному маршруту, его перемещения заданы программно.

## Для графического представления работы радара помимо языка Ардуино и написанного на нем скетча,  был использован язык программирования Processing, который является инструментом для программирования изображений и анимаций (своего рода альбомное программное обеспечение).

## Созданный проект может быть использован в охранной системе зданий, сооружений или каких-либо помещений. Кроме того, радар, как отдельный элемент, может быть применим для перемещения беспилотных автомобилей через систему автоматического управления, а так же удачно использован в системе парктроник.

Схема радара на макетной плате

Схема робота-солдата на макетной плате

Скетч робота-солдата

#include <IRremote.h> // подключаем библиотеку для IR приемника

#include <Servo.h> //используем библиотеку для работы с сервоприводом

Servo rightfoot;

Servo righthigh;

Servo leftfoot;

Servo leftthigh;

Servo lefthand;

Servo righthand;

int pos;

IRrecv irrecv(A0); // указываем пин, к которому подключен IR приемник

decode_results results;

void setup() // процедура setup

{

irrecv.enableIRIn();  // запускаем прием инфракрасного сигнала

rightfoot.attach(10);

righthigh.attach(9);

leftfoot.attach(8);

leftthigh.attach(7);

lefthand.attach(12);

righthand.attach(13);

Serial.begin(9600); // подключаем монитор порта

}

void loop() // процедура loop

{

if (irrecv.decode(&results)) // если данные пришли выполняем команды

{

Serial.println(results.value); // отправляем полученные данные на порт

if (results.value == 0xFF30CF) {

rightfoot.write(45);

delay (30);

lefthand.write(75);

righthand.write(75);

leftfoot.write(105);

delay (250);

lefthand.write(60);

righthand.write(60);

leftthigh.write(105);

delay (250);

lefthand.write(45);

righthand.write(45);

rightfoot.write(105);

delay (250);

lefthand.write(30);

righthand.write(30);

righthigh.write(105);

delay (250);

lefthand.write(15);

righthand.write(15);

leftfoot.write(90);

rightfoot.write(85);

lefthand.write(15);

righthand.write(15);

}

if (results.value == 0xFF18E7) {

rightfoot.write(85);

righthigh.write(90);

leftfoot.write (90);

leftthigh.write(90);

lefthand.write(90);

righthand.write(90);

;

}

if (results.value == 0xFF7A85) {

leftfoot.write(130);

delay (30);

lefthand.write(15);

righthand.write(15);

rightfoot.write(67);

delay(200);

lefthand.write(45);

righthand.write(45);

righthigh.write(75);

delay (250);

lefthand.write(85);

righthand.write(85);

leftthigh.write(75);

delay (200);

lefthand.write(125);

righthand.write(125);

leftfoot.write (90);

delay (250);

lefthand.write(150);

righthand.write(150);

rightfoot.write(85);

}

if (results.value == 0xFF10EF) {

rightfoot.write(45);

delay (30);

leftfoot.write(105);

delay (250);

leftthigh.write(105);

delay (250);

rightfoot.write(105);

delay (250);

righthigh.write(105);

delay (250);

leftfoot.write(90);

rightfoot.write(85);

}

if (results.value == 0xFFC23D)  {

rightfoot.write(45);

delay (30);

lefthand.write(75);

righthand.write(75);

leftfoot.write(105);

delay (250);

lefthand.write(60);

righthand.write(60);

leftthigh.write(105);

delay (250);

lefthand.write(45);

righthand.write(45);

rightfoot.write(105);

delay (250);

lefthand.write(30);

righthand.write(30);

righthigh.write(105);

delay (250);

lefthand.write(15);

righthand.write(15);

leftfoot.write(90);

rightfoot.write(85);

lefthand.write(15);

righthand.write(15);

delay (1000);

leftfoot.write(130);

delay (30);

lefthand.write(15);

righthand.write(15);

rightfoot.write(67);

delay(200);

lefthand.write(45);

righthand.write(45);

righthigh.write(75);

delay (250);

lefthand.write(85);

righthand.write(85);

leftthigh.write(75);

delay (200);

lefthand.write(125);

righthand.write(125);

leftfoot.write (90);

delay (250);

lefthand.write(150);

righthand.write(150);

rightfoot.write(90);

delay (1000);

rightfoot.write(45);

delay (30);

lefthand.write(75);

righthand.write(75);

leftfoot.write(105);

delay (250);

lefthand.write(60);

righthand.write(60);

leftthigh.write(105);

delay (250);

lefthand.write(45);

righthand.write(45);

rightfoot.write(105);

delay (250);

lefthand.write(30);

righthand.write(30);

righthigh.write(105);

delay (250);

lefthand.write(15);

righthand.write(15);

leftfoot.write(90);

rightfoot.write(85);

lefthand.write(15);

righthand.write(15);

delay (1000);

leftfoot.write(130);

delay (30);

lefthand.write(15);

righthand.write(15);

rightfoot.write(67);

delay(200);

lefthand.write(45);

righthand.write(45);

righthigh.write(75);

delay (250);

lefthand.write(85);

righthand.write(85);

leftthigh.write(75);

delay (200);

lefthand.write(125);

righthand.write(125);

leftfoot.write (90);

delay (250);

lefthand.write(150);

righthand.write(150);

rightfoot.write (90);

delay (1000);

}

irrecv.resume(); // принимаем следующий сигнал на ИК приемнике

}

}

Скетч радара на Arduino

#include <Servo.h>

#define pisk 3

const int trigPin = 10;

const int echoPin = 11;

long duration;

int distance;

Servo myServo;

void setup() {

pinMode(pisk, OUTPUT);

pinMode(trigPin, OUTPUT);

pinMode(echoPin, INPUT);

Serial.begin(9600);

myServo.attach(12);

}

void loop() {

for(int i=15;i<=165;i++){

myServo.write(i);

delay(25);

distance = calculateDistance();

Serial.print(i);

Serial.print(",");

Serial.print(distance);

Serial.print(".");

}

for(int i=165;i>15;i--){

myServo.write(i);

delay(25);

distance = calculateDistance();

Serial.print(i);

Serial.print(",");

Serial.print(distance);

Serial.print(".");

}

}

int calculateDistance(){

int val , frecuency;

digitalWrite(trigPin, LOW);

delayMicroseconds(2);

digitalWrite(trigPin, HIGH);

delayMicroseconds(10);

digitalWrite(trigPin, LOW);

duration = pulseIn(echoPin, HIGH);

distance= duration*0.034/2;

if (distance<40){

analogWrite(pisk, 500);

delay(100);

} else{

analogWrite(pisk,0);

delay(100);

}

return distance;

}

Скетч радара на Processing

import processing.serial.*;

import java.awt.event.KeyEvent;

import java.io.IOException;

Serial myPort;

String angle="";

String distance="";

String data="";

String noObject;

float pixsDistance;

int iAngle, iDistance;

int index1=0;

int index2=0;

PFont orcFont;

void setup() {

size (1366, 700);

smooth();

myPort = new Serial(this,"COM4", 9600);

myPort.bufferUntil('.');

}

void draw() {

fill(98,245,31);

noStroke();

fill(0,4);

rect(0, 0, width, 1010);

fill(98,245,31);

drawRadar();

drawLine();

drawObject();

drawText();

}

void serialEvent (Serial myPort) {

data = myPort.readStringUntil('.');

data = data.substring(0,data.length()-1);

index1 = data.indexOf(",");

angle= data.substring(0, index1);

distance= data.substring(index1+1, data.length());

iAngle = int(angle);

iDistance = int(distance);

}

void drawRadar() {

pushMatrix();

translate(683,700);

noFill();

strokeWeight(2);

stroke(98,245,31);

// draws the arc lines

arc(0,0,1300,1300,PI,TWO_PI);

arc(0,0,1000,1000,PI,TWO_PI);

arc(0,0,700,700,PI,TWO_PI);

arc(0,0,400,400,PI,TWO_PI);

// draws the angle lines

line(-700,0,700,0);

line(0,0,-700*cos(radians(30)),-700*sin(radians(30)));

line(0,0,-700*cos(radians(60)),-700*sin(radians(60)));

line(0,0,-700*cos(radians(90)),-700*sin(radians(90)));

line(0,0,-700*cos(radians(120)),-700*sin(radians(120)));

line(0,0,-700*cos(radians(150)),-700*sin(radians(150)));

line(-700*cos(radians(30)),0,700,0);

popMatrix();

}

void drawObject() {

pushMatrix();

translate(683,700);

strokeWeight(9);

stroke(255,10,10); // kırmızı renk

pixsDistance = iDistance*22.5;

// 40 cm ye kadar ölçer

if(iDistance<40){ line(pixsDistance*cos(radians(iAngle)),-pixsDistance*sin(radians(iAngle)),700*cos(radians(iAngle)),-700*sin(radians(iAngle))); } popMatrix(); } void drawLine() { pushMatrix(); strokeWeight(9); stroke(30,250,60); translate(683,700); line(0,0,700*cos(radians(iAngle)),-700*sin(radians(iAngle))); popMatrix(); } void drawText() { pushMatrix(); if(iDistance>40) {

noObject = "Out of Range";

}

else {

noObject = "In Range";

}

fill(0,0,0);

noStroke();

rect(0, 1010, width, 1080);

fill(98,245,31);

textSize(25);

text("10cm",800,690);

text("20cm",950,690);

text("30cm",1100,690);

text("40cm",1250,690);

textSize(40);

text("Object: " + noObject, 240, 1050);

text("Angle: " + iAngle +" °", 1050, 1050);

text("Distance: ", 1380, 1050);

if(iDistance<40) {

text("        " + iDistance +" cm", 1400, 1050);

}

textSize(25);

fill(98,245,60);

translate(390+960*cos(radians(30)),780-960*sin(radians(30)));

rotate(-radians(-60));

text("30°",0,0);

resetMatrix();

translate(490+960*cos(radians(60)),920-960*sin(radians(60)));

rotate(-radians(-30));

text("60°",0,0);

resetMatrix();

translate(630+960*cos(radians(90)),990-960*sin(radians(90)));

rotate(radians(0));

text("90°",0,0);

resetMatrix();

translate(760+960*cos(radians(120)),1000-960*sin(radians(120)));

rotate(radians(-38));

text("120°",0,0);

resetMatrix();

translate(840+900*cos(radians(150)),920-960*sin(radians(150)));

rotate(radians(-60));

text("150°",0,0);

popMatrix();

}